## Slide 1: Delta Wing with Vortex Breakdown Johan Kok (NLR) and Marian Fuchs (CFDB)
28-30/09/2015
Go4Hybrid Final Workshop, Berlin

## Slide 2: Test case definition
NASA delta wing
  Chu & Luckring (1996)
  65° leading-edge sweep
  sharp leading edge
  used in VFE-2
  stepping Stone in ATAAC
Selected flow condition
  vortex breakdown
  , ,
Experiment by TU München
  includes pressure and velocity fluctuations
  Furman & Breitsamter (2008, 2009)

## Slide 3: Characterization of flow
Shear layer separates from sharp leading edge and rolls up into primary vortex
At high Reynolds, shear layer becomes unstable and turbulent vortex is formed
At high angle of attack, primary vortex breaks down (high axial velocity in core drops to zero)
Possible secondary, pressure-induced separation (between primary vortex and leading edge)
Grey areas:
  shear layers emanating from leading edges
  initial vortex near apex

## Slide 4: Grids
Common multi-block structured grid (from ATAAC)
  6.3 Mcells (mandatory) + 21.4 Mcells (fine)
  mesh size ≈ 0.003 to 0.011cmac
  far field: 3 root chords
  conical structure: refined towards apex (learned in ATAAC)

## Slide 5: Available reference data
Experiment of TU München:
  Steady surface pressure at five chord stations: x/cr = 0.2, 0.4, 0.6, 0.8, and 0.95
  Unsteady surface pressure at four chord stations: x/cr = 0.4, 0.6, 0.8, and 0.95
  Stereo-PIV (mean velocity field) at five chord stations: x/cr = 0.2, 0.4, 0.6, 0.8, and 0.95
  HWA (fluctuating velocity field) at three chord stations: x/cr = 0.4, 0.6, and 0.8
  (Oil flow visualization)
Experimental data provided by Christian Breitsamter (TU München)

## Slide 6: Computations performed
CFDB:
  baseline: standard SA-DDES + Δmax
  GAM: SA-σ-DDES + (GAM)
  2nd-order blended central/upwind scheme
NLR:
  baseline: standard SST-DDES
  GAM: DX-LES + HPF + stochastic backscatter SGS model
  4th-order low-dispersion skew-symmetric finite-volume method
Common
  mandatory grid
  2nd-order implicit time integration
  CTU (convective CFL )
  1300 time steps per period of dominant frequency (St )
  transient about 7 CTU; statistics about 15 CTU

## Slide 7: Instantaneous vortical structures
SA-DDES + Δmax
SA-σ-DDES +
SST-DDES
HPF DX-LES
NLR
CFDB
steady helical structures
unsteady fine structures

## Slide 8: Mean pressure coefficient
GAM methods:
improved suction peak of main vortex

## Slide 9: RMS of pressure coefficient
GAM methods:
improved pressure fluctuations

## Slide 10: Resolved turbulent kinetic energy – baseline methods
x/c = 0.4
x/c = 0.6
x/c = 0.8
Experiment (HWA)
NLR SST-DDES
CFDB SA-DDES
no resolved turbulence

## Slide 11: Resolved turbulent kinetic energy – GAM methods
x/c = 0.4
x/c = 0.6
x/c = 0.8
Experiment (HWA)
NLR HPF DX-LES
CFDB SA-σ-DDES
improved resolved turbulence

## Slide 12: Time-averaged velocity field – baseline methods
Experiment (PIV)
NLR SST-DDES
CFDB SA-DDES
x/c = 0.4
x/c = 0.6
x/c = 0.2
vortex breakdown too early
vortex higher/stronger

## Slide 13: Time-averaged velocity field – GAM methods
Experiment (PIV)
NLR HPF DX-LES
CFDB SA-σ-DDES
x/c = 0.4
x/c = 0.6
vortex breakdown delayed
x/c = 0.2

## Slide 14: Time-averaged velocity field – baseline methods
x/c = 0.6
Experiment (PIV)
NLR SST-DDES
CFDB SA-DDES
vortex breakdown too early
x/c = 0.8
vortex breakdown
x/c = 0.95

## Slide 15: Time-averaged velocity field – GAM methods
x/c = 0.6
Experiment (PIV)
NLR HPF DX-LES
CFDB SA-σ-DDES
x/c = 0.8
vortex breakdown delayed
x/c = 0.95
vortex breakdown

## Slide 16: I2 Delta wing – Conclusions
GAM methods give very similar results
  CFDB (SA-σ-DDES + )
  NLR (DX-LES + HPF + stochastic backscatter SGS model)
Strong improvement by GAM methods, in particular in terms of levels of pressure fluctuations and resolved turbulence
As a result, GAM delays vortex breakdown Breakdown location closer to PIV measurements

## Slide 18: Experiment: Time-averaged velocity field and turbulent kinetic energy
HWA: k
x/c = 0.4
x/c = 0.6
x/c = 0.8
PIV: mean u
HWA: mean u
early vortex breakdown induced by HWA?
vortex breakdown