## Slide 1: Proposal for round jet test case
Charles Mockett
CFD Software GmbH
charles.mockett@cfd-berlin.com
With support from NTS

## Slide 2: Outline (notes)
Intro (pronounced GA / Applications / Partners )
Proposed test case (Shur config / G3 (variation opt.) / BC / Focus on flow – far-field noise optional)
Benchmark data (Bridges / Viswanathan)
Envisaged investigations
  Non-zonal GA treatment
  Situation for embedded approaches not clear (UniMan?)

## Slide 3: Introduction
Hybrid RANS-LES of turbulent jet flows have very pronounced Grey Area
Benchmark test case for jet noise applications
Partners contributing:
  CFDB (coordinators)
  NLR
  NTS
  UniMAN
Proposal for concrete test case definition presented
  Formulated in collaboration with NTS

## Slide 4: Proposed test case
M = 0.9, unheated, static jet, ReD = 1.1∙106, D = 0.06223 m
Studied extensively by NTS
  Shur et al., Journal of Sound & Vibration 330 (2011) 4083-4097
  Two-step approach
    RANS of jet & plume followed by ILES of plume
    Inside of nozzle not meshed: RANS solution imposed at nozzle outlet plane
NTS grids and nozzle plane profiles will be made available to Go4Hybrid partners

## Slide 5: Grids
4 different grid resolutions
Coarse grid shown – hybrid H/O topology
Slice x = D
Slice z = 0

## Slide 6: Grids
Grid | Nx | Nr | Nφ | Cell count
G1 | 308 | 81 | 64 | 1.6M
G2 | 515 | 101 | 80 | 4.2M
G3 | 515 | 101 | 160 | 8.4M
G4 | 601 | 158 | 240 | 23M
G3 proposed as mandatory
  Gives reasonable results at feasible numerical cost
Computation of grid study encouraged
  Robustness of method to insufficient shear layer resolution

## Slide 7: Benchmark data
For mean flow / turbulence characteristics (mandatory)
  Measured in a number of studies
  Significant scatter
  “Consensus” data proposed by Bridges
For far-field noise (optional)
  Measurements of Viswanathan appear most reliable

## Slide 8: Mean streamwise velocity

## Slide 9: Fluctuations of streamwise velocity

## Slide 10: Far field sound

## Slide 11: Remarks on method suitability
Non-zonal approaches
  Assumes coupled simulation of nozzle and plume
  However only plume is meshed
  “Emulation” of real situation by imposing RANS solution at nozzle
  The test case seems suitable
Embedded approaches
  Very thin boundary layer would make WMLES resolution inside nozzle unfeasibly expensive
  Negligible turbulence levels in core flow
  Questionable whether this case is suitable for embedded approaches
    => UniMAN?

## Slide 12: Thank you for your attention
Feedback? Questions?